## Slide 1: Audience/Audio Basics
For small venues (~20-30 people or less) House Audio is Not Required BUT may be used if available
Use of the built-in laptop microphone is not recommended
The recommended wireless microphone system supports all presenter styles
  Podium/fixed
  Lavaliere
  Headset
Set up wireless mic’s and receiver in accordance with system manual
Recommend headset mic for presenter and handheld for audience

## Slide 2: Connection to PC and Mixer
Use of balanced cables is only necessary with very long cable runs or when the audio cable is run alongside ac power cables

## Slide 3: CASE 1 - No house audio (small group) Hookup to Camtasia PC Only

## Slide 4: CASE 2 - Using House audio With access to mixer

## Slide 5: CASE 3 - Using House audio WITHOUT access to mixer

## Slide 6: Microphone and Recording Basics
Distance/Position is everything!
Each Microphone has different/unique requirements
Handheld dynamic microphone 4” ~45 degrees out of plane

## Slide 7: Lavaliere (midline as close to throat as possible)

## Slide 8: Headset - corner of mouth, flat/front of transducer facing and parallel to face

## Slide 9: Putting it all together
Make a short test recording
Check level, clarity
5 volume/gain controls
Avoid highest gains due to potential distortion
Troubleshooting